## Slide 1
Detailed project workflow (7/14/2020)
Simulation Scheme
Training Scheme
GCP
Cloud computing on google cloud platform (GCP). Virtual machine running on an NVIDIA Tesla P100 16GB GPU
Images
Labels
codes.txt
valid.txt
Train.ipynb
Predict.py
Write out classes by hand
codes.txt :
Car
Person
Tree
…
create_valid.py
Exported model
Experimental data
AWS filtering
Thickness segmentation map
Wavenumber map
Analysis and Validation
valid.txt :
List of .png files in validation set
Data
Labeling software
Label format: grayscale segmentation mask, where pixel values = class code
Start
Finish
Key:
Missing component
Jump to slide
Directory
Filename
(details)
Deployment path
augmentation

## Slide 2
Simulation scheme
 | Round 1 |  | Round 2 (example) |  | Round … | 
Parameters | Constant or Variable | Value | Constant or variable | Value |  | 
Mesh size | Constant | 5 mm | Constant | 5 mm |  | 
Mesh shape | Constant | Quadrilateral | Constant | Quadrilateral |  | 
Plate size | Constant | 400x400 mm | Constant | 400x400 mm |  | 
Plate material | Constant | Aluminum (type?) | Constant | Aluminum |  | 
Plate thickness | Constant | 10 mm | Variable | 1,3,5,7,9 |  | 
Transducer frequency | Constant | 80 kHz | Constant | 80 kHz |  | 
Transducer location | Constant | Center | Variable | 3x3 grid |  | 
Number of defects | Constant | 4 | Variable | 1,2,3,4 |  | 
Defect thickness | Variable | 2,4,6,8 mm | Constant | ... |  | 
Defect location | Variable | Orientation 1 and 2 | Constant | ... |  | 
Defect shape | Variable | Square, Circle, V rect, H rect | Constant | ... |  | 
Defect size | Variable | 40x40mm, 50 mm dia., 40x10mm, 10x40mm | Constant | ... |  | 
Round 1
CAD (Solidworks, FreeCAD)
Parameters
ANSYS harmonic response
Surface-Deformation.txt
Matlab image processing
224 image dataset
Round 2
CAD (Solidworks, FreeCAD)
Matlab image processing
Home

## Slide 3
Training scheme
 |  | Round 1: small images | Round 2: big images
Parameters | Variable name | Value | Value
Image shape | size | Original // 2 | Original
Batch size | bs | 16 | 4
Weight decay | wd | 0.01 | 0.01
Starting percent | pct_start | 0.3 | 0.3
Stage 1: train last layer only
Run lr_find()
Set learning rate lr to steepest slope
fit_one_cycle(10, slice(lr))
Save model
‘stage-1-small.pth’
Stage 2: train all layers
Images
Labels
codes.txt
valid.txt
Train.ipynb
Unfreeze model
Run lr_find() and set lr range
fit_one_cycle(12, slice(low, lr/5))
Save model
‘stage-2-small.pth’
Stage 1: train last layer only
Run lr_find()
Save model
Stage 2: train all layers
Unfreeze model
Save model
Round 1
Round 2
Export model
‘export.pkl’
Home

## Slide 4
Google Cloud Platform (GCP)
Create a Google Cloud Platform account
Launch a Deep Learning VM: https://console.cloud.google.com/marketplace/details/click-to-deploy-images/deeplearning?pli=1
Use all of the settings at Fast.AI: https://course.fast.ai/start_gcp.html
  Don’t make preemptible
Use NVIDIA Tesla P100 16 GB GPU
Increase GPU quota: https://stackoverflow.com/questions/45227064/how-to-request-gpu-quota-increase-in-google-cloud
  Search “GPUs (all regions)” and request quota=1
Create a conda virtual environment: https://docs.conda.io/projects/conda/en/latest/user-guide/tasks/manage-environments.html
Setup static IP to connect to VM through a browser and Jupyter notebook: https://towardsdatascience.com/running-jupyter-notebook-in-google-cloud-platform-in-15-min-61e16da34d52
SSH to VM instance through the GCP console (click SSH after starting the VM)
Activate virtual environment and open the Train.ipynb in a Jupyter Notebook
Connect to this notebook via a browser on your host computer
All edits will be saved on the VM
Upload dataset to the VM and run the Train.ipynb notebook
Download all results and desired output to host computer
Stop the VM instance after each use
Home