## Slide 1
Thicknesses
1,2,3,4,5,6,7,8,9,10 mm
1-9 mm defects
Shapes
90, 80, 70, 60, 50, 40, 30 , 20, 10 % thickness reductions
10 different classes
3 different shapes
Constants
80 kHz
Aluminum
400 x 400 mm plate
40 mm transducer
ANSYS parameters (damping ratio, pressure, mesh size)

## Slide 2
Location of defect (round 4)
9 locations
9 thicknesses
3 shapes
= 243 simulations
180 deg (x2)
486 images total
(Horizontal + vertical flipping + gaussian noise
all will happen on-the-fly during training)

## Slide 3
Location of transducer
(round 5)
4 locations
9 thicknesses
1 circle defect (50mm)
= 36 simulations
180 deg (x2)
72 images total

## Slide 4
Defect size
(round 6)
9
8
7
6
5
4
3
2
Plate thickness
Thickness at defect
8,7,6,5
7,6,5,4
6,5,4,3
5,4,3,2
4,3,2,1
3,2,1
2,1
1
Size = 10,30,50,70, 90 mm
1 shape (square)
26 plate+defect combos
= 130 simulations
180 deg (x2)
260 total images

## Slide 5
Plate thickness
(round 7)
4 transducer locations
10 thicknesses
= 40 simulations
180 deg (x2)
80 total images

## Slide 6
Big edge defects
(round 8)
6 edge defect widths (10,20,30,40,50,60mm)
9 thicknesses
= 54 simulations
180 deg (x2)
108 total images

## Slide 7
Defect location
Transducer location
Defect size
Plate thicknesses
Large edge defects
Total:
Augmented total:
Simulations
243
36
130
40
54
503
1006
Test cases
Unbounded
Delamination
Regression (continuous)
Noise (SNR)
VeRy sMaLl defects (<10mm)
Multiple defects
Layered defects
Irregular shape
Could be included in training set if needed
To test generalizability of model / future areas of work
Only 180 rotation. Could double again with Gaussian noise
rd4_shape_thickness_locx_locy.png
rd5_thickness_locx_locy.png
rd6_plateThickness_defectThickness_defectSize.png
rd7_plateThickness_locx_locy.png
Rd8_plateThickness_edgewidth.png

## Slide 8
Noise
Unbounded
Thickness decreases
Enclosed defects (delamination)
Continuous changes (regression)
Big edge defects
Multiple defects
Layered defects
Irregular defects

## Slide 9
Noise study
Size of defect study
Frequency invariance
Material
Experimental data
Regression
Custom CNN model to improve accuracy
Improve CNN
Test batchnorm v. normal accuracy
IoU and F1 score against published values
Batch size
Weight decay
Percent start
Validation transforms
Number of epochs
Augmentation v. no augmentation v. on the fly
More work